ABSTRAK

PENGARUH BAHAN DAN VARIASI JARAK ELEKTRODA TERHADAP KELISTRIKAN YANG DIHASILKAN LIMBAH JERUK PURUT

Fajar Maulana

Penelitian ini adalah penelitian eksperimen. Penelitian dengan tujuan untuk membuktikan tingkat keasaman jeruk purut dapat dijadikan sebagai energi listrik. Dengan pembuatan sebuah baterai volta yang rangkaian elektrodanya divariasikan, sehingga dapat diketahui secara langsung energi yang dihasilkan. Alat ini akan dijadikan sebagai alat bantu ajar/praktikum dalam materi ajar kelistrikan. Dengan baterai volta jeruk purut, siswa akan mudah memahami konsep terjadinya listrik dengan ionisasi, beda potensial, katoda-anoda, rangkaian tunggal-seri-paralel-dan campuran, serta tegangan.

Populasi dalam penelitian ini adalah limbah jeruk purut dipasar, jeruk yang sudah tidak baik fisiknya dimanfaatkan sebagai bahan utama elektrolit pada baterai volta. Sebagai elektroda yang digunakan dalam pembuatan rangkaian ialah bervariasi seperti plat seng, tembaga, timah, aluminium, dan besi, selain mudah dicari semua plat ini juga memiliki beda potensial yang besar. Untuk pembuatan prototipe dan penelitian dilakukan di Laboratorium Fisika UMN Al-Washliyah, dengan menggunakan alat yang dibutuhkan pembuatan alat dapat terselesaikan dengan cepat.

Dari hasil penelitian yang dilakukan, diperoleh data yang cukup memuaskan. Air jeruk purut memilki tingkat keasaman atau pH yang stabil yaitu 2,2. Perbedaan rangkaian dan jenis elektroda memperlihatkan hasil yang sangat sesuai dengan teori yang berlaku. Yaitu dengan hasil luaran listrik yang didapatkan pada rangkaian paralel 0.7 volt, rangkaian seri pasangan seng - tembaga 4.3 volt, pasangan timah - tembaga 1.6 volt, pasangan besi - tembaga 2 volt, pasangan aluminium - tembaga 1.9 volt, hasil perhitungan rangkaian campuran 4,2 volt dan hasil perhitungan jarak elektroda sebesar 0.7 volt. Dari hasil penelitian yang dilakukan dapat disimpulkan bahwa baterai volta dengan elektrolit jeruk purut dapat membantu guru untuk memahamkan siswa tentang materi kelistrikan, sehingga dapat meningkatkan hasil belajar siswa dan memberikan motivasi agar siswa dapat menyukai mata pelajaran fisika dengan pembuktian konsep sederhana fisika.

ABSTRACT

THE EFFECT OF MATERIALS AND VARIATIONS OF ELECTRODE DISTANCE TO ELECTRICITY THAT ARE PRODUCED BY SEA WASTE

Fajar Maulana

This research is experimental research. Research with the aim of proving the acidity of kaffir lime can be used as electrical energy. By making a voltaic battery whose electrode circuit is varied, so that it can be known directly the energy produced. This tool will be used as a teaching aid / practicum in electrical teaching materials. With kaffir lime voltaic batteries, students will easily understand the concept of the occurrence of electricity with ionization, potential differences, cathodes, anode-parallel-series and mixtures, and voltages.

The population in this study is kaffir lime waste in the market, oranges that are not physically good are used as the main material of electrolytes in voltaic batteries. As the electrodes used in making the circuit are varied such as zinc plate, copper, tin, aluminum, and iron, in addition to easy to find all these plates also have a large potential difference. For the manufacture of prototypes and research carried out at the UMN Al-Washliyah Physics Laboratory, using the tools needed to make the tool can be solved quickly.

From the results of the research conducted, obtained quite satisfactory data. Kaffir lime has a stable acidity or pH of 2.2. Differences in the series and types of electrodes show results that are very in accordance with the prevailing theory. That is with the output of electricity obtained in a 0.7 volt parallel circuit, a series of zinc pairs - copper 4.3 volts, a pair of tin - copper 1.6 volts, a pair of iron - copper 2 volts, a pair of aluminum - copper 1.9 volts, the calculation of mixture circuit 4.2 volts and the calculation of the electrode distance is 0.7 volts. From the results of the research conducted, it can be concluded that voltaic batteries with kaffir lime electrolytes can help teachers to understand students about electrical material, so that it can improve student learning outcomes and provide motivation so students can like physics with proof of simple physics concepts.